## Slide 1: Distributing Content Simplifies ISP Traffic Engineering
Abhigyan Sharma*
Arun Venkataramani* Ramesh Sitaraman*~
*University of Massachusetts Amherst
~Akamai Technologies
Notes: I am Abhigyan from Umass Amherst,
Title of my talk
Arun Ramesh
This work is with my advisors Arun Venkataramani and Ramesh Sitaraman. Ramesh is also affiliated with Akamai Technologies.

## Slide 2: Tripartite view of content delivery
CDN
Networks
Content providers
NCDN
NCDN
NCDNs deployed in 30+ ISPs globally
NCDN
Notes: Relatively nascent
CDN & Networks are collaborating, CDNs are licensing their technology to networks licensed & managed

## Slide 3: NCDN Management
Traffic Engineering
Content Distribution
NCDN Mgmt.
Optimize routing
to remove congestion hotspots
Optimize
content placement
&
request redirection
to improve
user-perceived performance
Notes: Avoid congestion hotspots in the network
Traffic engineering and content distribution are not independent problems. How an NCDN does placement affects its routing decisions and vice versa?

## Slide 4: NCDN Routing Placement Interaction
B
C
A
D
8 Mbps
4 Mbps
0.5 Mbps
1.5 Mbps
Demand = 1 Mbps
Demand = 0.5 Mbps
Maximum link utilization (MLU) = 0.75/1.5 = 0.5
1.25 Mbps
0.25 Mbps
0.25 Mbps
0.75 Mbps
Traffic labeled with flow value
Link labeled with capacity
Notes: No MPLS!
The difference is that, for an NCDN, content distribution and traffic engineering are no longer independent problems.
For example, how an NCDN places the content on its network affects its traffic engineering objectives.
I will explain this point using an example.
In this four node network, link capacities are as shown.
Lets say there is a content cache at node C where a single MPEG video file is stored. This video file has a demand of 1 Mbps at node A & 0.5 Mbps at node D, and there is no other traffic.
To minimize the maximum link utilization in this case, the traffic should be routed as follows.
To effect this routing, we need to use MPLS which splits traffic in the ratio 1:3 between the two paths CBA & CDA.

## Slide 5: NCDN Routing Placement Interaction
B
C
A
D
8 Mbps
4 Mbps
0.5 Mbps
1.5 Mbps
Demand = 1 Mbps
Demand = 0.5 Mbps
Maximum link utilization (MLU) = 1/8 = 0.125
Traffic labeled with flow value
Link labeled with capacity
0.5 Mbps
1 Mbps
  Content placement flexibility reduces network costs and enables simpler routing
Notes: Unlike traditional TE model, where an ISP has no control over content placement, an NCDN has the flexibility to place content. Lets say an NCDN leverages this power to place content also at node B.
--------------------------------------------------------------------------------------------------------
Placement
Much smaller MLU
Transition: Now lets take a step back and take an overview of design space of NCDN schemes.
The difference is that, for an NCDN, content distribution and traffic engineering are no longer independent problems.
For example, how an NCDN places the content on its network affects its traffic engineering objectives.
I will explain this point using an example.
In this four node network, link capacities are as shown.
Lets say there is a content cache at node C where a single MPEG video file is stored. This video file has a demand of 1 Mbps at node A & 0.5 Mbps at node D, and there is no other traffic.
To minimize the maximum link utilization in this case, the traffic should be routed as follows.
To effect this routing, we need to use MPLS which splits traffic in the ratio 1:3 between the two paths CBA & CDA.

## Slide 6: NCDN Schemes Classification
Unplanned
(e.g. LRU Caching)
Traffic
Engineering
Content Distribution
Joint Optimization
Planned
(history-based)
Planned
(e.g. OSPF weight tuning)
Unplanned (static routing)
NCDN Management
Notes: OSPF: widely used shortest path routing protocol
Planned: makes its decisions using recent history of content popularity across the network, e.g., content popularity measured over the previous day
Static routing: What ever be the traffic demands, routing remains the same.
This slide shows the classification of schemes applicable to an NCDN.
At the top level, NCDN management involves content distribution and traffic engineering.
For content distribution, we consider two types of schemes: unplanned and planned.
An unplanned scheme uses a simple online algorithm to decide content placement and request redirection. An example of a unplanned content placement strategy is Least-recently-used or LRU caching.
A planned scheme decides placement of content and request redirection based on a recent history of content popularity in different parts of the network.
Coming to traffic engineering, we similarly consider planned and unplanned strategies.
A planned traffic engineering computes and optimized routing based a recently measure traffic matrix. An example is OSPF weight tuning algorithm proposed by Fortz and Thorup.
An unplanned traffic engineering uses a statically configured routing oblivious of the traffic matrix. A simple example which we evaluate in the paper is OSPF with inverse capacity link weights.
Based on this classification, an NCDN management can use any combination of planned and unplanned strategies.
In addition, the class of joint optimization strategies jointly optimize content distribution and traffic engineering. You can think of them as a combination of planned content distribution and planned traffic engineering.
This classification is by no means exhaustive, for example, you can do content distribution using a hybrid of planned and unplanned strategies.
Based on this classification, I am going to raise three questions which are central to identifying the right NCDN management schemes.
%To give an example, in the paper we consider an MIP based formulation which optimizes a content distribution metric given content popularity over the previous day at each node and other constraints such as storage available at nodes.

## Slide 7: Research Questions
How do simple unplanned schemes perform?
Is joint optimization better than other schemes?
What matters more: placement or routing?
Notes: Is joint optimization necessary?
Here are the questions:
Read out the questions.
Now let see how do we go about answering these questions.
First, we define a NCDN model.

## Slide 8: Outline
Network CDN
NCDN Model & Joint Optimization
Datasets: Akamai Traces & ISP Topologies
Results
Related Work
Notes: In this part of the talk, I am going to explain several classes of NCDN management schemes, giving representative examples of schemes in each class.
%Also, I will give a sketch of our NCDN model and problem formulation.

## Slide 9: NCDN Model
Downstream end-users
9
Origin servers
NCDN POP
Content servers
Backbone router at
exit nodes
Backbone router
Notes: This slide shows the POPs of an NCDN
Add flying content
In this slide, I am going to talk about our NCDN model while describing how a user’s request is served by an NCDN.
This slide shows Points of presence (POPs) of an NCDN connected using ISP backbone links.
An NCDN PoP is similar to an ISP PoP, except it is equipped with content servers.
Requests from down stream end users first reach the content servers at the nearest PoP.
The content servers serve the users immediately if content is available locally at these servers.
Otherwise, If content is available at nearby NCDN PoPs, the PoP fetches the content, cache content locally and serve the request,
If content is unavailable at any PoP in the NCDN, it is fetched from the content provider’s origin servers, cached locally and serve the request.
We model two resource constraints for an NCDN.
First constraint is the storage at each PoP and second constraint is the capacity of the backbone links.
Based on this NCDN model, lets see how we formulate the joint optimization problem for NCDNs

## Slide 10: NCDN Model
Downstream end-users
10
Origin servers
NCDN POP
Content servers
Backbone router at
exit nodes
Backbone router
Notes: This slide shows the POPs of an NCDN
Add flying content
In this slide, I am going to talk about our NCDN model while describing how a user’s request is served by an NCDN.
This slide shows Points of presence (POPs) of an NCDN connected using ISP backbone links.
An NCDN PoP is similar to an ISP PoP, except it is equipped with content servers.
Requests from down stream end users first reach the content servers at the nearest PoP.
The content servers serve the users immediately if content is available locally at these servers.
Otherwise, If content is available at nearby NCDN PoPs, the PoP fetches the content, cache content locally and serve the request,
If content is unavailable at any PoP in the NCDN, it is fetched from the content provider’s origin servers, cached locally and serve the request.
We model two resource constraints for an NCDN.
First constraint is the storage at each PoP and second constraint is the capacity of the backbone links.
Based on this NCDN model, lets see how we formulate the joint optimization problem for NCDNs

## Slide 11: NCDN Model
Downstream end-users
11
Origin servers
NCDN POP
Content servers
Backbone router at
exit nodes
Backbone router
Notes: This slide shows the POPs of an NCDN
Add flying content
In this slide, I am going to talk about our NCDN model while describing how a user’s request is served by an NCDN.
This slide shows Points of presence (POPs) of an NCDN connected using ISP backbone links.
An NCDN PoP is similar to an ISP PoP, except it is equipped with content servers.
Requests from down stream end users first reach the content servers at the nearest PoP.
The content servers serve the users immediately if content is available locally at these servers.
Otherwise, If content is available at nearby NCDN PoPs, the PoP fetches the content, cache content locally and serve the request,
If content is unavailable at any PoP in the NCDN, it is fetched from the content provider’s origin servers, cached locally and serve the request.
We model two resource constraints for an NCDN.
First constraint is the storage at each PoP and second constraint is the capacity of the backbone links.
Based on this NCDN model, lets see how we formulate the joint optimization problem for NCDNs

## Slide 12: NCDN Model
Downstream end-users
12
Origin servers
ISP backbone
link capacity
Resource constraints
POP storage
Notes: This slide shows the POPs of an NCDN
Add flying content
In this slide, I am going to talk about our NCDN model while describing how a user’s request is served by an NCDN.
This slide shows Points of presence (POPs) of an NCDN connected using ISP backbone links.
An NCDN PoP is similar to an ISP PoP, except it is equipped with content servers.
Requests from down stream end users first reach the content servers at the nearest PoP.
The content servers serve the users immediately if content is available locally at these servers.
Otherwise, If content is available at nearby NCDN PoPs, the PoP fetches the content, cache content locally and serve the request,
If content is unavailable at any PoP in the NCDN, it is fetched from the content provider’s origin servers, cached locally and serve the request.
We model two resource constraints for an NCDN.
First constraint is the storage at each PoP and second constraint is the capacity of the backbone links.
Based on this NCDN model, lets see how we formulate the joint optimization problem for NCDNs

## Slide 13: NCDN Joint Optimization
Hardness
  Theorem 1: Opt-NCDN is NP-Complete even in the special case where all objects have unit size, all demands, link capacities and storage capacities have binary values.
Approximability
  Theorem 2: Opt-NCDN is inapproximable within a factor β for any β > 1 unless P = NP.

## Slide 14: MIP for Joint Optimization
Objective:
  Minimize NCDN-cost (MLU or latency)
Constraints:
  For all node: total size of content < Storage capacity
  For all (content, node): demand must be served from POPs or origin
Output variables:
  Placement: Binary variable iXY indicates whether content X is stored at node Y
  Redirection
  Routing
Notes: Minimize an NCDN cost function
The inputs to the joint optimization are the storage and link capacity values and the “content matrix”. Each entry in the content matrix shows the demand for a content at a PoP in the network.
NCDN management problem outputs three variables: content placement, request redirection and routing.
We have some theoretical results about this problem:
NCDN management combines traffic engineering & content distribution into a single formulation. It outputs three variables: content placement, request redirection and routing, and its inputs are the content matrix and the storage and link capacity constraints.
All the NCDN management schemes we evaluate conform to the formulation presented in this slide.
Before we go to the schemes and their formulation, let us take a quick look at the Akamai datasets we use for out evaluation

## Slide 15: Outline
Network CDN
NCDN Model & Joint Optimization
Datasets: Akamai Traces & ISP Topologies
Results
Related Work
Notes: In this part of the talk, I am going to explain several classes of NCDN management schemes, giving representative examples of schemes in each class.
%Also, I will give a sketch of our NCDN model and problem formulation.

## Slide 16: Datasets
Akamai traces | 
Traffic types | On-demand video & download
How measured? | Instrument client software, e.g., media player plugin
Data | Content URL, content provider, lat-long, timestamp, bytes downloaded, file size
Volume | 7.79 m users, 28.2 m requests, 1455 TB data
ISP topologies | 
Networks | Tier-1 US ISP & Abilene
Data | POP lat-long, link capacities
Mapping: Akamai trace  ISP topology | 
Map request to geographically closest ISP POP | 
Notes: As we do not have access to an NCDN trace, we use a CDN trace to emulate NCDN traffic.
--------
Here are some quick facts from the data we collected from the Akamai CDN.
We collected traces for two different traffic classes: on-demand video and download. We selected these classes because they account for a majority of network traffic seen in a typical CDN.
Our traces include content from several major Akamai customers.
On-demand video contains several forms of long and short videos, from News clips to TV Shows to Movies.
Download consists of several types of content including software updates, …
On-demand video traces are collected during Oct 2011 & Jan 2012, and download traces are collected in Dec 2010.
Both traces are collected using client side measurements but the mechanism is bit different for the two classes.
On-demand video uses a plugin embedded in the media player running in the web browser.
Download traces are collected using a download manager embedded in client’s software, e.g., Apple iTunes or Microsoft Update.
On-demand video trace are collected from 6.59 million unique users in the US who downloaded 638 TB of video.
Download trace are collected from 0.62 million users in the US who downloaded 717 TB of content.

## Slide 17: Outline
Network CDN
NCDN Model & Joint Optimization
Datasets: Akamai Traces & ISP Topologies
Results
  Schemes Evaluated
  Network Cost
  Latency Cost
  Network Cost: Planned vs. Unplanned Routing
Related Work

## Slide 18: Schemes Evaluated
Scheme | Routing + placement + redirection
UNPLANNED | OSPF with link-weight = 1/link-capacity + LRU caching + redirect to closest hop count node
JOINT-OPTIMIZATION | Realistic joint optimization Once per day with yesterday’s content demand
ORACLE | Ideal joint optimization Once per day with current day’s content demand
Notes: Oracle is unachievable
The three schemes listed here are based on the classification described earlier.
InvCap-LRU uses unplanned content distribution and unplanned traffic engineering. The simplest of the three schemes. It uses Inverse Cap routing. It uses a LRU cache replacement strategy at each node. On a cache miss, requests are redirected to cache which has a copy of the content and is closest in terms of hop count distance.
Joint-Opt uses a planned joint optimization of content distribution and traffic engineering. This optimization is done once each day based on content matrix measured the previous day.
Joint-Opt-Future is similar to Joint-Opt but assumes an accurate future knowledge of content matrix over the next day. Joint-Opt-Future is a somewhat unachievable but is a useful scheme to benchmark the performance of the other two schemes.
To evaluate how these scheme perform in practice, we need a real traces of users accessing content on their networks.
For which, we have collected user-level logs of content access in the Akamai CDN.

## Slide 19: Network Cost
Chart: Tier-1 ISP Topology, Entertainment Trace
| 1.0 | 2.0 | 4.0
Joint Optimization | 1 | 0.81434 | 0.61968
Unplanned | 0.59947 | 0.36332 | 0.21031
Oracle | 0.37371 | 0.24622 | 0.17443
3x
18%
Notes: As storage ratio increases, Unplanned moves close to IDEAL, JOINT OPTIMIZATION still has a high MLU even at higher storage.
Why planned bad?
************************ move banner to slide ************************
This slides compares the schemes based on their network cost.
The two Joint-Opt scheme solve an MIP formulation to optimize the network cost.
The metric shown on the x-axis is storage ratio. A storage ratio of ‘k’ means that total storage across all PoPs is ‘k’ times the total size of unique content observed on a typical day.
The y-axis shows the network cost metric MLU normalized with respect to the highest MLU value.
As storage ratio increases, content can be replicated at more locations resulting in lower MLU.
We find that Joint-Opt has a 3x higher MLU than the simple unplanned scheme.
Why does Joint-Opt worse than the simple InvCap-LRU scheme. This is because Joint-Opt implements a planned content placement, request redirection and routing using a content matrix measured over the previous day.
All CDN traces we experiment with have a significant amount of churn in content even on a daily basis, and a significant fraction of requests are for new content published that day. Therefore, a planned approach perform needs to frequently fetch content from origin servers, which increases utilization of links along the path to the origin servers.
We have also evaluated other variations of Joint-opt such as combining Joint-Opt with InvCap-LRU and running Joint-Opt scheme multiple times per day, but Joint-Opt has a higher network cost than InvCap-LRU in those experiments as well.

## Slide 20: Latency Cost
Chart: Tier-1 ISP Topology, Entertainment Trace
| 1.0 | 2.0 | 4.0
Joint Optimization | 13990884.8306 | 903669.168 | 885326.0493
Unplanned | 1227893.0134 | 901201.1325 | 667501.1508
Oracle | 702086.0831 | 583356.4605 | 521214.505
Latency Cost = E2E propagation delay + Link utilization dependent delay
28%
Content placement matters tremendously in NCDNs
Notes: Transition:
What these experiments placement matters in NCDNs.
JOINT-OPTIMIZATION poor at content placement: performs worse.
UNPLANNED placement works well, and performs well.
Next question is does routing matter?
------------------------------------------
Lets go back to an earlier question I had raised.
In this experiment, we evaluate the user perceived latency for different schemes.
An equally important metric for an NCDN is the latency experienced by end-users, which we evaluate in this experiment.
To calculate latency, we have defined a latency cost function which captures the end-to-end delay including propagation delay and delay caused by retransmissions after a packet loss.
The value of the latency cost function is shown on the y-axis. X-axis is the storage ratio.
In this experiment, the two Joint-Opt schemes optimize for latency indicated by the letter L after their names.
The relative performance of schemes reflects a similar trend with the latency cost function as with the network cost function.
Joint-Opt strategy has a high latency cost for two reasons, first its higher MLU causes more retransmissions, and second it frequently needs to fetch content from origin servers which also increases latency.
InvCap-LRU performs better than a Joint-Opt strategy. InvCap-LRU improves its performance relative to the Joint-Opt-Future scheme on increasing the storage ratio. At a storage ratio of 4, the latency of InvCap-LRU is within 28% of Optimal while than Joint-Opt strategy has a 70% higher latency cost than optimal.
This experiment shows than an unplanned scheme has a close to optimal latency cost at higher storage ratios.

## Slide 21: Network Cost: Planned vs. Unplanned Routing
Chart: Tier-1 ISP topology, all traces
News | -2.8844
Entertainment | -5.168
Download | 9.9204
10% or less
Unplanned placement, unplanned routing
vs.
Unplanned placement, planned routing
Traditional TE gives small cost reduction in NCDNs
Notes: ** optimizing routing does not reduce network cost my much. **
Routing matters little in NCDNs
Placement
The last set of results evaluate the relative importance of optimizing content placement vs. that of optimizing routing.
The left graph shows how much does network cost reduce if we use an optimized routing instead of InvCap routing along with an unplanned LRU placement..
This optimized routing is calculated every three hours based on the traffic matrix observed in the previous three hours
We find that the maximum reduction is less than 10%, suggesting that optimizing routing brings minimal improvement over InvCap-LRU scheme.
While the left graph shows the result for an unplanned placement, the right graph shows the result for a planned placement scheme, and we take the Joint-Opt-Future which the ideal planned scheme.
We evaluate the importance of jointly optimizing content distribution and routing over optimizing only the content distribution but using InvCap routing.
Again we find that whether InvCap routing is used or routing is jointly optimized with content distribution makes only a 13% difference to MLU.
Overall, this results shows that after content placement is optimized, further optimizing routing adds little value.

## Slide 22: Related Work
ISP-CDN joint optimization of routing & redirection (with fixed placement) [Xie ‘08, Jiang ‘09, Frank ’12]
Optimize placement (with fixed routing) for VoD content [Applegate ’10]
Location diversity even with random placement significantly enhances traditional TE [Sharma ’11]
Notes: ***************** Joint optimization of x & y ******************
The first category of work is on ISP traffic engineering, starting with the work by Fortz and Thorup, who proposed the traffic engineering algorithm by tuning OSPF weights.
Following that is the work which studies the interaction of overlay routing and network routing. For example, Qiu et al showed that selfish overlay routing can negatively influence traffic engineering and increase network costs.
The third category includes work on optimization of content placement and redirection in CDNs. A recent work is that of Applegate et al, who show how to place content optimally for large number of content.
Finally, there is work on co-operation between ISPs and CDNs, such as P4P and CaTE, which shows that a joint optimization improves both content distribution performance and network cost. However, much of this work focuses only optimizing the redirection component of content distribution, and not the content placement.
In this work, we have studied NCDN management which combines content placement, redirection and traffic engineering into one problem. We find that content placement is extremely powerful in shaping the traffic in the network, so much that even simple unplanned strategies for routing and content distribution can achieve close to best latency and network costs for a CDN.

## Slide 23: Conclusions
Keep it simple
  Joint optimization performs worse than simple unplanned
  Little room for improvement over simple unplanned
Content placement matters more than routing in Network CDNs
Notes:     ** placement more important than routing **
    Planned strategies perform poorly, even hybrid strategy and other demand-aware schemes
    Simple demand-aware aware schemes perform surprisingly well, and on provisioning more storage Content placement is useful